## Slide 1
IBM BOB HACKATHON · TEAM ASTRA · AI TRACK
AeroReady
Mission Readiness & Predictive Maintenance Platform
LSTM MAE 10.05 cycles · R² 0.897 · 14 sensors monitored · 5 IBM Bob MCP tools
Notes: Welcome to AeroReady — a Mission Readiness and Predictive Maintenance platform built by Team Astra for the IBM Bob Hackathon, AI Track. We predict turbofan engine RUL with a validated LSTM model, classify 14 sensors with Isolation Forest anomaly detection, compute go/no-go mission readiness decisions, and surface all of it through a conversational Copilot and IBM Bob MCP tools.

## Slide 2
01 / THE PROBLEM
Aviation maintenance is expensive and reactive
💸 AOG events cost fleet operators $150K–$500K per day in lost revenue
📅 Fixed time-based maintenance schedules waste resources or miss genuine degradation
❓ No fast, data-driven answer to "Is this engine safe for today's mission?"
🔍 Sensor data exists but is not interpreted — buried in raw CSV files
The question is not whether the engine will fail — it's when, and whether that's before or after the mission.
Notes: Unplanned aircraft-on-ground events are one of the most costly problems in aviation maintenance. Operators today rely on fixed schedules that are either too conservative (wasting maintenance resources) or too relaxed (missing real degradation). The raw sensor data exists on every flight — it just isn't being used to answer the critical operational question: is this specific engine ready for this specific mission?

## Slide 3
02 / THE SOLUTION
AeroReady: sensor data → go/no-go decision in seconds
1 INGEST
Upload C-MAPSS CSV → idempotent DB load
2 PREDICT RUL
LSTM 30-cycle window → cycles remaining
3 SENSOR HEALTH
IForest 5-cycle window → NORMAL / DEGRADING / ABNORMAL
4 READINESS
margin = RUL - mission_duration → SAFE / MARGINAL / CRITICAL
5 COPILOT
NL question → evidence-grounded answer from DB
Key differentiator: deterministic Copilot — every statement cites a real DB value. No LLM. No hallucination. Works offline.
Notes: AeroReady is a 5-stage pipeline. The operator uploads a CSV; the LSTM predicts how many cycles remain; the Isolation Forest classifies each of the 14 sensors; the mission readiness engine computes whether there's enough margin for the planned mission; and the Copilot answers natural-language questions grounded in the actual database values — no generative AI, no hallucination risk, no API key needed.

## Slide 4
03 / TECHNICAL ARCHITECTURE
Full-stack ML system — proven on NASA C-MAPSS
ML PIPELINE
LSTM (2-layer, hidden=64, dropout=0.2)
Input: (batch, 30, 14)
Output: RUL in cycles (clipped at 125)
MAE 10.05 | R² 0.897
5-fold Group K-Fold validation
Isolation Forest (100 estimators, contamination=0.01)
Trained on RUL > 100 (healthy baseline)
14 sensor channels classified per engine
BACKEND
Flask 3.0 + Waitress (WSGI)
SQLAlchemy ORM + SQLite / PostgreSQL
6 DB models | 13 REST API endpoints
Layered arch: routes → controllers
→ services → repositories → models
Background threads for async ML inference
FRONTEND + BOB
React 18 + Vite + TailwindCSS
6 pages: Fleet, Asset Health, Alerts,
Maintenance, Reports, AI Copilot
Recharts for data visualisation
IBM Bob MCP (FastMCP)
5 tools: fleet summary, engine
readiness, sensor health, priority
engines, ask copilot
Notes: The technical stack is a fully integrated Python + JavaScript system. The ML layer uses PyTorch for the LSTM and scikit-learn for the Isolation Forest — both pre-trained on NASA C-MAPSS data. The Flask API sits in the middle with a clean layered architecture. The React frontend shows live data from the DB. And the FastMCP server gives IBM Bob read access to the entire system through five structured tools.

## Slide 5
04 / MISSION READINESS COPILOT
Natural-language fleet intelligence — zero hallucination
Operator asks:
"Is Engine 5 ready for the mission?"
Copilot responds:
"Engine 5 has MARGINAL mission readiness. Predicted RUL is 45.2 cycles with only 15.2 cycles of margin — below the recommended 20-cycle buffer. Additionally, 2 sensor(s) are degrading. Proceed with caution or consider maintenance before deployment."
How it works: keyword routing → 7 response handlers → templated answer from DB values → evidence dict returned
No LLM · No API key · Works offline · Every claim traceable to a database record
Notes: The Mission Readiness Copilot is the centrepiece of the Bob integration. It accepts any natural-language question about an engine and routes it to one of 7 response handlers. Each handler builds its answer from live database values — RUL, sensor states, margins, maintenance priority — and returns both the answer string and a 16-field evidence dictionary so every claim can be verified. No generative AI is involved — this means no hallucination, no API costs, and full offline operation.

## Slide 6
05 / IBM BOB INTEGRATION
AeroReady fleet data, interrogated from Bob
5 MCP TOOLS (src/mcp_server/server.py · registered via .bob/mcp.json)
get_fleet_summary → KPIs: total engines, ready, warning, high-priority count
get_engine_readiness → Full readiness report for one engine (RUL, margin, risk flag)
get_sensor_health → All 14 sensor states for one engine
list_high_priority_engines → Engines with HIGH maintenance priority
ask_copilot → Natural-language question → evidence-grounded answer
Bob: "Which engines need immediate attention before tomorrow's mission?"
AeroReady: [calls list_high_priority_engines + ask_copilot] → structured answer from live data
Architecture: IBM Bob → .bob/mcp.json → FastMCP server → Flask REST API → SQLite DB + ML models
Notes: The IBM Bob integration is implemented as a FastMCP server in src/mcp_server/server.py. The server is registered in .bob/mcp.json so Bob discovers it automatically. All 5 tools are thin HTTP wrappers over the existing Flask API — no logic is duplicated. Bob can interrogate the entire fleet, check individual engine readiness, inspect sensor states, and ask the Copilot natural-language questions — all from inside the Bob IDE.

## Slide 7
06 / RESULTS & TEAM
What we delivered — and what's next
10.05
MAE (cycles)
0.897
R² score
51 / 51
tests passing
5
IBM Bob MCP tools
Next steps: Multi-condition model (FD002/FD003/FD004) · Per-sensor independent IForest · Auth layer · Celery task queue · Cloud deployment
TEAM ASTRA — IBM BOB HACKATHON · AI TRACK
Source code: src/ · Docs: docs/ · MCP server: src/mcp_server/
setup guide: docs/setup-guide.md · 51 passing tests · Full architecture documented
AeroReady — Because a mission readiness decision should be justified, not guessed.
Notes: Summary: Team Astra built AeroReady — a complete end-to-end predictive maintenance and mission readiness system. The LSTM achieves MAE 10.05 cycles and R² 0.897 on NASA C-MAPSS. All 51 tests pass. The system is fully integrated with IBM Bob through 5 FastMCP tools. The next steps are real-world extensions: multi-condition training data, independent per-sensor anomaly models, authentication, and cloud deployment.